وزارة العمل

لجنة العطاءات الخاصة

الشروط والمواصفات الخاصة بالعطاء رقم (8/2019)

جهاز كمبيوتر رئيسي عدد (2)

مواصفات جهاز كمبيوتر رئيسي Quantity : 2

Intel Based Server

High quality brand name USA or ECC or Japan with the following minimum specifications

Form Factor : Rack

Server type : Intel Based

Processor : Two Intel Xeon silver 4110 8 core 2.1GHz, 11MB Cache

Memory : 64GB ECC DDR4, with memory protection expandable

Storages : 4 X 600 G SAS HOT Plug 15Krpm RAID Controller support RAID (0,1,10 and 5) ( hardware RAID ) with 1 GB Cache

Controllers : 2 x 1 GBit Ethernet Port, 2 x 10Gb/s Ethernet Port

Expansion and I/O : Min. 4 X USB , serial , VGA Min. 6 PCI-E Slots

Power and cooling : Fully used & redundant Hot-Pluggable power supplies 220-250 VAC/50Hz compatible with Jordan electricity standard Redundant Hot pluggable cooling Fans Enough cooling to enable working continuously (24/7) without overheating.

Management: Full Remote Management features.

Others : All Drivers that support the system should be provided as sent by manufacturer Original server management software, for installation and configuration.

Certified and/ or support : Microsoft windows server 2012 & Microsoft windows server 2016 Microsoft Hyper-V server 2012 / VMware VSphere latest RedHat Enterprise Linux

Registered Trade Mark : Must be specified

Country of origin certifications American , European or Japanese

Warranty :Three Years min. on site Parts And Labor